## Slide 1: SweetSpot Identification through Machine Learning for Unconventional Plays
Jingnan Xue
Summer 2015

## Slide 2: Agenda
 | Task Accomplished
1 | Universal Kriging
2 | 

## Slide 3
Universal Kriging
1.0

## Slide 4: Data aggregation
  For each variable in each core well, we have several measurements. Three methods can be applied to aggregate those measurements:
  Mean
  Trimmed Mean
    Calculated with only the middle 80% of the data
  Mean calculated without outliers
    IQR=Q3-Q1
    Values smaller than Q1-1.5IQR or larger than Q3+1.5IQR are identified as outliers

## Slide 5: kriging
  For each variable, Kriging can be used to predict its value in any production well based on the values in core wells.
  Kriging is a name for Best Linear Unbiased Prediction for spatial statistics
  Three Types of Kriging
    Simple kriging: when the mean is a known constant
    Ordinary kriging: when the mean is an unknown constant
    Universal kriging: when the mean is a function of covariates, the default case is a low-order polynomial function of locations. We use universal kriging in this project.

## Slide 6: Universal Kriging
  One example to show how to apply universal Kriging in R
  KrigTmax<-Krig(x=location, Y=Tmax)
    Location is an m2 matrix, recording the latitude&longitude of each core well
    Tmax is an m1 matrix, recording the aggregated Tmax at each core well
    This function produced a Kriging object which is used to do predictions
  predic.Tmax<-predict(KrigTmax,location)
    KrigTmax is the Kriging object produced before
    Location is a n2 matrix, recording the latitude&longitude of each production well
    This function produced a n1 matrix, recording the prediction of Tmax at each production well

## Slide 8
Data and workflow
2.0

## Slide 9: Data (EAGLE FORD)
  2631 oil production wells
  81 cored wells
Oil production & cored wells distribution

## Slide 10: Data (EAGLE FORD)
Production Heat Map

## Slide 11: WORKFLOW
Data Integration
Predictive Modeling
Raw Data
Normalized 1st 12-Month Production
Geological Feature Interpolated Map
Interpolation
Interpolated Feature Map
Preprocessing/
Outlier Removal
Stratigraphy Aggregate
Predictive Modeling
Core Analysis Data
Well Logs
Engineering Parameters
1st 12-mo. Production
Predictive Model

## Slide 12
PREDICTIVE MODELING
3.0

## Slide 13: RANDOM FOREST ALGORITHM
  Decision trees
X4 ≥ t4
X4 < t4
X3 ≥ t3
X3 < t3
X2 ≥ t2
X1 ≥ t1
X2 < t2
X1 < t1
X1
X2
X3
X4
C4
C3
C2
C1
C5
  Random Forest (ensemble decision trees)
    Non-parametric method without any distribution assumptions on x and y
    Can handle nonlinear relationships
    Provides effective methods for estimating missing data ...
13

## Slide 14: RESULTS (RF 5-Fold Cross-Validation)
Top 25% Wells True Production
Top 25% Wells Predicted
74% Overlap
Eagle Ford Oil Producer Sweetspots (658 out of 2631)
Correctly Identified TQ |  |  | 
Random Draw | Rule Based | Kaggle | RF
165 | 201 | 366 | 484
14
May 2015

## Slide 15: VARIABLE IMPORTANCE
Permutation-based MSE reduction measure normalized by the maximum score.
15
May 2015

## Slide 16: PREDICTION BASED ON TOP K IMPORTANT VARS
Top 7 important vars. are good enough to build a predictive model.
Correlation Tmax and Ro Calculated ~ 1, Ro Calculated is removed from the model.
A parsimonious model (6 vars.) achieved similar performance as full model (31 vars.)
{True vertical depth, S2, Tmax, Chlorite in clay(X-ray diffraction), Ro measured, GRI water filled porosity}
16
Results of 5-fold cross-validation
May 2015

## Slide 17: TOP QUANTILE RECOVERY CURVE
17
Results of 5-fold Cross-validation
Performance Comparison of Different Models
May 2015

## Slide 18: CHRONOLOGICAL STUDY
18
Producers with 12-mon production by the cutoff date will be used for training
Performance Comparison By Different Cutoff Date
Total 2631 Producers
2008-04-01 first producer start production
2013-09-01 last producer achieve 12-mon production
May 2015

## Slide 19: Concluding remark
  Going forward:
    Complete ML/DA modeling and prediction workflow in Q4 2015.
    Apply to active assets E&P in 2016 and beyond.
  Business Impact
    Provide superior guiding technology for new well drilling to reduce cost and improve production.
    Furnish quick and better methodology for new asset assessment.

## Slide 20
Q & A
20